## Slide 1: Introduction to Architecture Simulation
Shin-haeng Kang
shkang@iris.snu.ac.kr
2016-03-15

## Slide 2: SNUCSE Unified Account
http://www.snucse.org/Account/JoinForm.aspx

## Slide 3: Agenda
Why simulator?
Terminologies
Timing model
SystemC basic

## Slide 4: Why simulator?

## Slide 5: Simulation?
Imitation of the operation of a real-world process or system
  simulation of technology, safety engineering, testing, training, education, and video games
Need to build an appropriate simulation model.
  To represent the key characteristics or behaviors/functions of the selected system and process.

## Slide 6: Architecture Simulation
Design tomorrow’s architecture using today’s architecture
The most important tool available to computer architecture researchers
Purpose
  Obtain performance characteristics for new architectures
  Architectural exploration
  Early software development/optimization

## Slide 7: 1) Performance evaluation
Performance evaluation methodologies in papers appearing in the Proceedings of the International Symposium on Computer Architecture
27.9%
88%
87%

## Slide 8: 2) Architecture exploration
Find the optimal configuration
Cache set size
Cache line size
Associativity
Decision space
Cache miss ratio
Objective space
Power consumption
Simulation

## Slide 9: 3) Early software development/optimization
Simulators let you prototype, develop and test applications without using a physical device.
Example) A virtual mobile device emulator for Android
  mimics all of the hardware and software features of a typical mobile device, except that it cannot place actual phone calls

## Slide 10: Terminologies

## Slide 11: Host and target
Simulation host, simulation target
  Simulation host: the system executing simulation.
  Simulation target: the system being simulated.
  Ex ) The definition of Architecture simulation: to design tomorrow’s architecture using today’s architecture
Simulation time, simulated time
  Simulation time:
    Consumed during the computation of the simulation (wallclock time)
  Simulated Time
    Simulated within the simulation
  example) it takes 1000s (simulation time) on the simulation host to simulate 1s (simulated time) of the simulation target
Simulation target
Simulation host

## Slide 12: Cross-compile
[shkang@ubuntu example]$ arm-gcc -o hello_world hello_world.c
[shkang@ubuntu example]$ ./hello_world
-bash: ./hello_world: cannot execute binary file: Exec format error
[shkang@ubuntu example]$ tqsim hello_world
Hello world! I am an arm binary
------------------------------------------------------
-----------------Statistics---------------------------
------------------------------------------------------
Total commited inst : 12049
Estimated execution cycle : 37945
Cache il1] num_access: 2124 / num_miss: 303
Cache dl1] num_access: 4777 / num_miss: 185
Cache ul2] num_access: 488 / num_miss: 453
Bpred] num_lookups: 2822 / num_misses: 475
Definition: creating executable code for a simulation target system on which the compiler is running (=host system)
Creating ARM-executable binary on an x64 ubuntu machine
Simulation
Cross-compile

## Slide 13: Simulation categories (1)
Scope
  Instruction set simulator: can model a target microprocessor only
  Full system simulator: can model an entire computer system including a processor, a memory system, and I/O devices.
Focus
  Functional simulation
    Generates correct program output
    Validate only functional requirements
  Timing simulation
    captures the timing of events to obtain program execution time

## Slide 14: Simulation categories (2)
Input (workload)
  Trace-driven (event-driven): Simulator reads a “trace” of instructions captured during a previous execution
    Trace = time ordered record of events on real system
  Execution-driven: Simulator “runs” the program
2 408ed4
0 10019d94
2 408ed8
1 10019d88
2 408edc
0 10013220
2 408ee0
2 408ee4
1 100230b8
2 408ee8
0 10013220
2 408eec
2 408ef0
2 408ef4
1 10013220
2 408ef8
1 100230bc
2 408efc
Trace-based
Cache
Simulator
./dineroIV -l1-isize 16384 -l1-iassoc 4 -l1-ibsize 32 -l1-irepl l -l1-dsize 32768 -l1-dassoc 2 -l1-dbsize 16 -l1-drepl f -l1-dwalloc a -l1-dwback a -informat d < cc1.din > sample.out

## Slide 15: Simulation categories (3)
Abstraction level
  RTL (Register Transfer Level)
  TLM (Transaction Level Modeling)
    abstracts communication
CLK
ADDR
EN
DATA
nRW
MEMORY
CPU
Read
Write
Load
Execute
RTL module
RTL module
Functional Module
Functional Module
Pin_0 = 1
Pin_1 = 0
Pin_2 = 0
……
write(addr, data)
TLM
RTL

## Slide 16: Instruction set simulator (ISS)
Based on the instruction set architecture
Implemented in high level languages like C++
Modeling the behavior of microprocessors
  Reading instructions and maintaining internal variables which represent the processor's registers.
Categories
  Interpretive ISS
  Compiled ISS
    Static
    Dyanmic

## Slide 17: Interpretive ISS
Interpret an instruction one by one
Mimics the microarchitecture pipeline
Flexible & Accurate
  Working in the similar way to the processor behavior
  Easy to implement, easy to estimate performance
Slow
ruu_init()
for (;;) {
ruu_commit();
ruu_writeback();
lsq_refresh();
ruu_issue();
ruu_dispatch();
ruu_fetch();
}
Simplescalar’s main function
Simplescalar’s structure

## Slide 18: Statically Compiled ISS
Simulation compiler compiles the target binary to produce a C code to be executed on the host machine: reduce decoding time.
Fast
Cannot support dynamic program code
  Self-modifying code, external code (loading), dynamic linking library, and multiple instruction set (ARM:Thumb)
Large memory space
Target Code
Target Binary
Target Cross-Compiler
C Code generation
C code
Host executable Code
Host C-compiler

## Slide 19: Dynamic binary translation (DBT)
A runtime conversion of the target CPU instructions into the host instruction set.
Relative slow
Flexible and relatively accurate
Ex) QEMU
QEMU emulation flow
Target Binary
Inst Fetch
Binary Trans lation
Translation Cache
Execution
Cache hit?
Hit
False

## Slide 20: Dynamic binary translation (DBT)
0x00008d0c: e92d4800 push {fp, lr}
mov_i32 tmp5,r13
movi_i32 tmp6,$0xfffffffffffffff8
add_i32 tmp5,tmp5,tmp6
mov_i32 tmp6,r11
qemu_st_i32 tmp6,tmp5,leul,$0x0
……
Arm binary
(target binary)
Intermediate code
0x7f56b63fba10: mov -0x4(%r14),%ebp
0x7f56b63fba14: test %ebp,%ebp
0x7f56b63fba16: jne 0x7f56b63fbaba
0x7f56b63fba1c: mov $0x9380,%ebp
0x7f56b63fba21: mov %gs:0x0(%rbp),%ebp
0x7f56b63fba25: mov %ebp,0x8(%r14)
0x7f56b63fba29: mov %gs:0x0(%rbp),%ebp
…
x64 binary
(host binary)

## Slide 21: Timing model
Cycle-accurate simulation
k-CPI simulation
Analytical simulation
Sampled simulation
Statistical simulation
FPGA-accelerated simulation

## Slide 22: Cycle-accurate simulation
Simulates a microarchitecture on a cycle-by-cycle basis
  Update the system state every cycle
Slow
  10 – 100 KIPS (kilo simulated instructions per second)
100 KIPS
i7 Simulator
240 GIPS
Intel Core i7 5960X
To simulate 1s
240,000s is required
1.82 year

## Slide 23: k-CPI simulation
it takes k cycles to execute one instruction
The number of cycles is given
  By one cycle for all instructions (1-CPI model)
  According to the datasheet of the simulated processor (datasheet model)
Fastest but inaccurate
Ex) Imperas OVP and ARM FastModels

## Slide 24: Analytical simulation
Estimates the processor performance by using mathematical formulas
How construct a model?
  Mechanistic model: based on the mechanics of the target processor
    White-box modeling
  Empirical model: by machine learning or regression analysis
    Black-box modeling

## Slide 25: Sampled simulation
performs cycle-accurate simulation with sampling units rather than the entire instruction streams
Sampling units are selected
  randomly
  periodically
  based on phase analysis

## Slide 26: Statistical simulation
Uses generated short-running synthetic traces or benchmarks that are representative for long-running benchmarks
Statistics collection phase
  Base program characteristics: basic instruction mix and instruction dependency
  Micro-architectural dependent statistics: cache, branch statistics
Synthetic simulator phase
  Feed a synthetic instruction trace to a simple processor model

## Slide 27: FPGA-accelerated simulation
Implements timing models onto field-programmable gate-arrays (FPGA)
Demands an additional hardware and development time to synthesize the model into hardware

## Slide 28: Conclusion
Accuracy
Speed

## Slide 29: SystemC

## Slide 30: SystemC
A set of C++ classes and macros to support system-level design
Motivation
  Even Verilog or VHDL’s behavioral modeling is not high-level enough
  People generally use C or C++
Developed by OSCI (Open systemC initiative)
Open-source
  http://accellera.org/downloads/standards/systemc
Support both TLM and RTL modeling
  Does not have to use multiple languages to use multiple level of abstractions.

## Slide 31: SystemC supports
Concurrency
  Concurrent processes can be described using plain C++ syntax
Timing
  Clocks are special signals that run periodically and trigger clocked processes
Rich set of data types for HW

## Slide 32: SystemC design methodology
C, C++ System-level
Model
Analysis
Results
Verilog/VHDL
Simulation
Synthesis
Manual Translation
(Error-prone)
Previous design methodology
SystemC-based methodology
SystemC Model
Simulation
Refinement
Synthesis

## Slide 33: Introductory Example
Testbench
Counter
Clock
Module
Port
Channel
do_count
Reset
Go
value
process

## Slide 34: Module
Basic Unit of Design
Hierarchical Entity
Syntax
SC_MODULE(module_name) {
/* port declaration */
/* local channel(signal) declaration */
/* variable declaration */
/* process declaration */
/* other method declaration */
/* submodule declaration */
/* constructor */
SC_CTOR(module_name) {
/* module instantiation and channel binding */
/* process registration */
/* sensitivity list */
/* module variable initialization */
}
}

## Slide 35: Ports (pin-level)
Define the interface to each module
Three types of ports depending on the direction
  Input: sc_in
  Output: sc_out
  Bidirectional: sc_inout
Member functions
  read(): read the current value
  write(value): write a new value
  event(), pos()/neg()
Syntax
  sc_in{out,inout}<data_type> port_name;
  ex) sc_in<bool> clk, reset, go;

## Slide 36: Processes
 | SC_METHOD | SC_THREAD | SC_CTHREAD
Infinite loop | No | Yes | Yes
construct | SC_METHOD(pro) sensitive(sig); sensitive_pos(sig); semsitive_neg(sig); | SC_THREAD(pro); sensitive(sig); sensitive_pos(sig); semsitive_neg(sig); | SC_CTHREAD(pro, clock.pos()); SC_CTHREAD(pro. clock,neg());
suspend | NA | wait() | wait(); wait(n*);
local variable | lost | saved | saved
Static sensitivity | signal events | signal events | clock edge
Dynamic sensitivity | next_trigger(ev); | wait(ev) | wait_until(exp); watching(exp);
Usage | Comb. logic | Behavior, test bench | FSM

## Slide 37: Sensitivity List
Determine when to trigger the process
Static sensitivity: defined in SC_CTOR
  sensitive << event [<< event]…; //streaming style
  sensitive(event [, event]…); //functional style
Dynamic sensitivity: defined inside the process definition
  SC_METHOD: next_trigger(event)
  SC_THREAD: wait(event)
  SC_CTHREAD: wait_until(expression)
  SC_CTHREAD: watching(expression)
Defined on process registration to restart the process when the expression is met.

## Slide 38: Timing in SystemC
Time in SystemC
  units: SC_SEC, SC_MS, SC_US, SC_NS, SC_PS, SC_FS
  “sc_time” class defines a time object (ex) sc_time t(15, SC_NS)
  Define the time unit
    sc_set_default_time_unit(1, SC_NS): set the default time unit
    sc_set_time_resolution(1,SC_NS): set the default time resolution
      The default is SC_PS if omitted
  Keep track of the current simulation time: cout << sc_time_stamp()<<endl;
Clock
  The only thing in SystemC that has a notion of real time
  sc_clock name(“name”, period, duty_cycle, first, rising) or sc_clock name(“name”, period, time_unit, duty_cycle, first, first_time_unit, rising)
    first: time elapsed until encounters the first edge
    rising: set “TRUE” if the first edge is rising or “FALSE” if falling

## Slide 39: Channels (1)
SystemC has two types of channel : primitive and hierarchical
Primitive channels
  Contains no hierarchy, no processes.
  Designed to be very fast due to their simplicity.
  sc_signal, sc_buffer, sc_mutex, sc_fifo, sc_semaphore
module
process
Channel
port
interface
module
process
channel
process
interface
interface

## Slide 40: Channels (2)
Both supports 1 writer & multiple readers
Basic methods
  read(), write(), delayed(), event(), etc
Evaluate-update protocol
  New value is visible after the current process is suspended
Difference
  sc_buffer generates an event at every write() while sc_signal generates an event only when the value is changed.
  You will see the difference through the lab.

## Slide 41: SystemC module (revisited)

## Slide 42: Lab Notification
18th March, Friday
1-3 PM
Room 311-1, Building 302
Q) Do you have an SNUCSE Unified account?