## Slide 1: SystemC Lab
Shin-haeng Kang
shkang@iris.snu.ac.kr
Digital System Design Methodology
2016-03-18

## Slide 2: What am I missing in the previous class?
Statically compiled ISS?
When you need SystemC?
  Can you use legacy C code in SystemC?

## Slide 3: Types of Instruction set simulator
Target Binary
C Code generation
Intermediate C code
Host Executable Code
Host Code Build
Statically compiled ISS
Interpretive ISS
Look up translation cache
Single inst
All insts
Basic block
Interpret
Execute
Translated Cache
Execute
Dynamic binary translation (DBT)
Host Code Build

## Slide 4: Statically Compiled ISS vs Normal Compiling
Why is it for?
Target Binary
Intermediate C code
Host Executable Code
Target Code
Target Code
Host Executable Code
Host Compiler
Cross Compiler
C code Generation
Host Compiler
Functional simulation may be possible (unless target code contains target-specific code)
Characteristics of the target binary are gone away.
Both functional/timed simulation are possible
Characteristics of the target binary are preserved

## Slide 5: Example) Statically Compiled ISS

## Slide 6: SystemC
A set of C++ classes and macros to support system-level design
Motivation
  Even Verilog or VHDL’s behavioral modeling is not high-level enough
  People generally use C or C++
Developed by OSCI (Open systemC initiative)
Open-source
  http://accellera.org/downloads/standards/systemc
Support both TLM and RTL modeling
  Does not have to use multiple languages to use multiple level of abstractions.

## Slide 7: HDL and SystemC
SystemC deliberately mimics the hardware description languages VHDL and Verilog, but is more aptly described as a system-level modeling language.
SystemC is more on higher abstraction level than HDLs
SystemC is better for co-simulation of software firmware and hardware components.
You can focus on communications. You can program a process as you like in C++ semantics.
  Including stdin/stdout/stderr and C++ standard libraries

## Slide 8: TLM-style modeling
Motivation
  Increase simulation speed
  Reduce modeling effort
  Allow for easier model adaptability
  Enable efficient architecture exploration
  Enable parallel HW and SW development based in virtual prototypes
Measure
  Interaction between SystemC Modules is abstracted
  Function calls instead of signals
    Based on sc_interface

## Slide 9: SystemC with TLM
General characterization of a transaction between initiator and target in max. 4 phases
  Begin / end of request
  Begin / end of response

## Slide 10: Temporary LOG-IN ID and password
If you have your own, use it.
Otherwise, use a temporary login ID
  Choose Digital Systems Design Methodology
  Choose Not listed? -> type “dsdm2016”

## Slide 11: Server LOG-ID
Download an SSH application
  http://mobaxterm.mobatek.net/MobaXterm_v8.6.zip
Connect to tyrell.snu.ac.kr
Login ID
  Default password: “defaultpasswd”
  Change the default password to your owns.
Student ID | Login ID
30752 | Student01
81455 | Student02
82421 | Student03
22693 | Student04
31434 | Student05
21235 | Student06
31052 | Student14
31054 | Student15
21189 | Student16
21217 | Student17
21229 | Student18
30281 | Student19
21276 | Student07
22147 | Student08
22895 | Student09
22907 | Student10
23299 | Student11
31048 | Student12
31050 | student13

## Slide 12: Modules: Basic Unit of Design
Syntax (RTL style)
SC_MODULE(module_name) {
/* port declaration */
/* local channel(signal) declaration */
/* variable declaration */
/* process declaration */
/* other method declaration */
/* submodule declaration */
/* constructor */
SC_CTOR(module_name) {
/* module instantiation and channel binding */
/* process registration */
/* sensitivity list */
/* module variable initialization */
}
}

## Slide 13: Modules: Basic Unit of Design
Syntax (TLM style)

## Slide 14: SystemC Ports (pin-level)
Define the interface to each module
Three types of ports depending on the direction
  Input: sc_in
  Output: sc_out
  Bidirectional: sc_inout
Syntax
  sc_in{out,inout}<data_type> port_name;
  ex) sc_in<bool> clk, reset, go;

## Slide 15: SystemC Processes
Processes have sensitivity lists, i.e. a list of signals that cause the process to be invoked, whenever the value of a signal in this list changes.
method
  behaves like a function
threads
  Keeps executing or waiting for some event to occur.
cthread : a special thread.
  The sensitivity list is just the specified clock edge.

## Slide 16: SystemC Processes
 | SC_METHOD | SC_THREAD | SC_CTHREAD
Infinite loop | No | Yes | Yes
construct | SC_METHOD(pro) sensitive(sig); sensitive_pos(sig); semsitive_neg(sig); | SC_THREAD(pro); sensitive(sig); sensitive_pos(sig); semsitive_neg(sig); | SC_CTHREAD(pro, clock.pos()); SC_CTHREAD(pro. clock,neg());
suspend | NA | wait() | wait(); wait(n*);
local variable | lost | saved | saved
Static sensitivity | signal events | signal events | clock edge
Dynamic sensitivity | next_trigger(ev); | wait(ev) | wait_until(exp); watching(exp);
Usage | Comb. logic | Behavior, test bench | FSM

## Slide 17: Processes:examples

## Slide 18: Sensitivity List
Determine when to trigger the process
Static sensitivity: defined in SC_CTOR
  sensitive << event [<< event]…; //streaming style
  sensitive(event [, event]…); //functional style
Dynamic sensitivity: defined inside the process definition
  SC_METHOD: next_trigger(event)
  SC_THREAD: wait(event)
  SC_CTHREAD: wait_until(expression)
  SC_CTHREAD: watching(expression)
Defined on process registration to restart the process when the expression is met.

## Slide 19: Timing in SystemC
Time in SystemC
  units: SC_SEC, SC_MS, SC_US, SC_NS, SC_PS, SC_FS
  “sc_time” class defines a time object (ex) sc_time t(15, SC_NS)
  Define the time unit
    sc_set_default_time_unit(1, SC_NS): set the default time unit
    sc_set_time_resolution(1,SC_NS): set the default time resolution
      The default is SC_PS if omitted
  Keep track of the current simulation time: cout << sc_time_stamp()<<endl;
Clock
  The only thing in SystemC that has a notion of real time
  sc_clock name(“name”, period, duty_cycle, first, rising) or sc_clock name(“name”, period, time_unit, duty_cycle, first, first_time_unit, rising)
    first: time elapsed until encounters the first edge
    rising: set “TRUE” if the first edge is rising or “FALSE” if falling

## Slide 20: Channels (1)
SystemC has two types of channel : primitive and hierarchical
Primitive channels
  Contains no hierarchy, no processes.
  Designed to be very fast due to their simplicity.
  sc_signal, sc_buffer, sc_mutex, sc_fifo, sc_semaphore
module
process
Channel
port
interface
module
process
channel
process
interface
interface

## Slide 21: Channels (2)
Both supports 1 writer & multiple readers
Basic methods
  read(), write(), delayed(), event(), etc
Evaluate-update protocol
  New value is visible after the current process is suspended
Difference
  sc_buffer generates an event at every write() while sc_signal generates an event only when the value is changed.
  You will see the difference through the lab.

## Slide 22: Signals
Convey information between sub-modules within a module
Port of sub-module defines the direction of data transfer

## Slide 23: Test Bench Module and Main File

## Slide 24: SystemC Examples-1
Simple adder program
  Adder_method : SC_METHOD
  Adder_thread1 : SC_THREAD, sensitivity – clk
  Adder_thread2 : SC_THREAD, sensitivity – a, b
  Adder_thread3 : SC_THREAD, sensitivity – a, b, clk
  Adder_cthread : SC_THREAD
Compare SC_METHOD, SC_THREAD, SC_CTHREAD

## Slide 25: SystemC Examples-1
stimulus
do_stim
(SC_THREAD)
clk
A
B

## Slide 26: SystemC Examples-1
adder_method
do_adder
(SC_METHOD)
A
B
adder_thread1
do_adder
(SC_THREAD)
clk
A
B
C
C

## Slide 27: SystemC Examples-1
adder_thread2
do_adder
(SC_THREAD)
A
B
C
adder_thread3
do_adder
(SC_THREAD)
clk
A
B
C

## Slide 28: SystemC Examples-1
adder_cthread
do_adder
(SC_CTHREAD)
clk
A
B
C

## Slide 29: SystemC Examples-1
AD_M
(adder_method)
AD_T1
(adder_thread1)
AD_T2
(adder_thread2)
AD_T3
(adder_thread3)
AD_C
(adder_cthread)
STIM
(stimulus)
clock
(clock)

## Slide 30: SystemC Examples-1
Build the simulator
  export LD_LIBRARY_PATH=$LD_LIBRARY_PATH:/usr/local/systemc/lib-linux64
  g++ -O3 -Wall -Wno-deprecated -g -I/usr/local/systemc/include -c main.cpp
  g++ -O3 -Wall -Wno-deprecated -g -I/usr/local/systemc/include -L/usr/local/systemc/lib-linux64 -o run.x main.o -lsystemc -lm 2>&1 | c++filt
Execute
  ./run.x

## Slide 31: SystemC Examples-1 result
Gtkwave wave.vcd

## Slide 32: SystemC Examples-2
Simple signal generator and receiver
Compare sc_signal, sc_buffer
  Generator generates events: 5 (at 5), 6 (at 15), 6 (at 25), 7 (at 35), 8 (at 45)
receiver
generator
receiver
sc_signal
sc_buffer

## Slide 33: SystemC Examples-2

## Slide 34: SystemC Examples-2 result
$ g++ -O3 -Wall -Wno-deprecated -g -I/usr/local/systemc/include -c main.cpp $ g++ -O3 -Wall -Wno-deprecated -g -I/usr/local/systemc/include -L/usr/local/systemc/lib-linux64 -o run.x main.o -lsystemc -lm 2>&1 ¦ c++filt $ ./run.x SystemC 2.3.1-Accellera --- May 15 2015 17:35:02 Copyright (c) 1996-2014 by all Contributors, ALL RIGHTS RESERVED 0 s:REV_BUF got 0 5 ns:REV_SIG got 5 5 ns:REV_BUF got 5 15 ns:REV_SIG got 6 15 ns:REV_BUF got 6 25 ns:REV_BUF got 6 35 ns:REV_SIG got 7 35 ns:REV_BUF got 7 45 ns:REV_BUF got 7

## Slide 35: Homework
By using SystemC, make your own components, test, and generate waveforms.
  1)16bit counter
  2) memory (size = 0x1000)
Deliverables
  Report
    Module design diagram
    Source code (module + testbed)
    Simulation result (including waveforms)
  Tarball
    Modules
    Testbed
    Working makefile
How to deliver
  shkang@iris.snu.ac.kr
  Title of the mail: [DSDM16] 20XX-XXXX homework submission
Deadline: 1st April